## Slide 1
Optical flow you can query:
calibrated confidence and 27x cheaper
repeat access for 2.6% of mean accuracy
Shriman Raghav Srinivasan
MS Robotics, Northeastern University | Field Robotics Lab
Final project presentation | 12 August 2026
Notes: I replaced NeuFlow v2's fixed upsampler with a decoder you can query at any coordinate. The headline is that this buys three capabilities v2 cannot express, and costs 2.6 percent of mean accuracy. I will show you both sides. The result I would most like your reaction to is selective accuracy, which is slide ten, so I will keep the earlier material tight.

## Slide 2
2
Most consumers use a few hundred of the
479,232 values a network computes
Registration picks a few hundred textured points, and needs flow there.
Sparse tracking needs flow at detected keypoints only.
Mosaicking needs matches in overlap regions, often between pixels.
On constrained hardware, computing 479,232 correspondences to consume 800
is the difference between operating in real time and not.
Frame size 384 x 1248. Baseline: Zhang et al. (2024), NeuFlow v2.
Notes: Every modern flow network computes a displacement for every pixel at one fixed resolution, and that contract is rarely questioned. It does not match what several important consumers actually need. Registration, sparse tracking and survey mosaicking all select a few hundred points themselves and discard the rest. On a small GPU that waste is the difference between real time and not.

## Slide 3
3
Can the output stage be made queryable
without surrendering accuracy or speed?
Can NeuFlow v2’s fixed upsampler be replaced by a decoder evaluated
at arbitrary continuous coordinates, and what does that cost?
Approach: freeze everything in v2 that understands motion; change only the last stage.
Consequence: cost scales with the number of queries, O(N), not with image area.
Evaluated on 1,174 held-out Virtual KITTI 2 pairs (460,573,660 px) and on TartanAir aerial sequences.
Notes: So the question this project answers, stated precisely. Not whether I can build a better flow network, but whether the final stage of a real-time one can be made queryable, and what that costs. The approach is to keep everything that understands motion frozen and change only the output, so the comparison isolates one variable.

## Slide 4
4
v3 keeps NeuFlow v2 frozen and replaces
only its fixed upsampler
Phase 1 · once per frame pair, 33 ms, cached
Image pair
>
CNN backbone
1/8, 1/16
>
Cross-attention
global match
>
Refinement
1x s16, 8x s8
>
Coarse flow
at 1/8
Phase 2 · once per query batch, 1.25 ms, O(N)
Query (x, y)
continuous
>
Sample 3x3
4 sources
>
Gated fusion
MLP
>
Convex blend
9 + 1
>
Flow and
confidence
The output is a convex combination of neighbouring coarse-flow values, so the decoder
cannot predict motion its inputs do not locally support.
Convex-weight formulation follows Jung et al. (2023), AnyFlow. Gated fusion follows InfiniDepth (2025).
Notes: The change is confined to the last stage. Phase one is v2 exactly as published, run once and cached. Phase two takes a coordinate, samples feature windows around it, and predicts weights that blend the nine neighbouring coarse flow values plus a bilinear sample. Because it is a convex blend it cannot hallucinate motion. And because phase one is cached, asking a second question about the same frame is cheap. That caching turns out to be the property that matters most.

## Slide 5
5
The front end is verified bit-identical to v2,
so the comparison isolates the decoder
Frozen front end. All 137 shared tensors bit-identical, per checkpoint.
Leak-free splits. Both test scenes excluded from every training set.
One variable per run. Same seed, schedule and query budget throughout.
Evaluation
Held-out pairs
1,174
Valid pixels
460.6 M
Cross-domain
TartanAir
Hardware
RTX 4060
Precision
fp16
Zero-initialised, the decoder is
exactly bilinear upsampling.
Cabon et al. (2020), Virtual KITTI 2; Wang et al. (2020), TartanAir.
Notes: Two things make the rest of the deck interpretable. First, the front end is frozen and I verify per checkpoint that all 137 shared tensors are bit-identical to v2, so any difference you see is the decoder and nothing else. Second, both evaluation scenes are excluded from every training set, checked at pair and frame level before each run. The zero-init property is worth noting too: an untrained decoder is exactly bilinear upsampling, so training can only move away from a known-good operating point by learning something.

## Slide 6
6
The decoder costs 2.6 percent of mean error,
from a model 13 percent smaller
What to take away
Every v3 configuration sits above v2.
Like-for-like on FlyingChairs: 2.500, or 7.6% behind.
7.83 M parameters against 9.03 M.
2.384 against 2.324
Mean end-point error, per pixel, 1,174 held-out VKITTI 2 pairs. Lower is better.
Notes: Here is the central cost, and I am leading with it rather than burying it. Every v3 configuration is less accurate than the baseline on mean end-point error. The best is 2.384 against 2.324, so 2.6 percent worse. The like-for-like comparison, trained on FlyingChairs alone as v2 was trained on FlyingThings alone, is 7.6 percent behind. The model is 13 percent smaller, which is worth something but does not excuse it. Four slides on, the same model is more than twice as accurate as v2 over most of the frame, once it is allowed to abstain. That is the argument.

## Slide 7
7
The cost concentrates in sub-pixel precision,
not in large errors
Diagnosed cause
Its finest input is 1/8 scale, so evidence barely varies inside an 8x8 cell.
Fourier positional encoding changed nothing, ruling out a missing position signal.
1.5 points below v2
Percentage of pixels with end-point error below 1 px. Higher is better.
Notes: This is where the cost actually sits. On one-pixel accuracy v3 is below v2 in every configuration. Mean error partly hides it, because v3 makes fewer catastrophic errors, which drags the average down while it is less exact on the majority of pixels. I know the mechanism: the decoder's finest input is at one-eighth resolution, so inside an eight by eight cell it is looking at almost the same evidence wherever you query, while the v2 upsampler reads the full-resolution frame directly. I tested the competing explanation, that it was simply missing positional information, by adding a Fourier encoding. It changed nothing, which rules that out.

## Slide 8
8
A repeat query on a cached frame costs
1.25 ms, against 33.3 ms for a fresh pass
Where the win is
A first sparse query is level with v2: both pay the coarse pass.
v2 keeps no state, so a second question costs a full recomputation.
27x on repeat access
RTX 4060 laptop, fp16, 384 x 1248, median of 50 runs after warm-up.
Notes: On speed I want to be precise about which claim I am making. Dense output is ten percent slower than v2, and that mode is not what the decoder is for. A first sparse query is level with v2, because 96 percent of the cost is the coarse pass, which both share and which cannot be skipped since global matching needs the whole image. The win is repeat access. Asking a second question about a frame you have already processed costs 1.25 milliseconds against 33.3, because v2 keeps no state and has to redo everything. Anything that revisits a frame gets that: iterative registration, RANSAC refinement, an operator inspecting a scene. That is structural, not a margin.

## Slide 9
9
Predicted confidence tracks real error
monotonically across a 15-fold span
Why it is usable
Weight correspondences in RANSAC by predicted scale.
Reject unreliable matches before they reach a solver.
v2 emits flow alone; there is no equivalent quantity.
0.48 px to 7.10 px
Per-query error scale under a Laplace likelihood. 2,348,000 queries, Pearson r = 0.318.
Notes: The head predicts an error scale for every query alongside the flow itself, trained under a Laplace likelihood. When you bin queries by predicted uncertainty, actual error rises monotonically across all five bins, from 0.48 pixels in the most confident to 7.10 in the least, a fifteen-fold span, over 2.35 million queries. It is not perfectly correlated, r is 0.318, but it is clearly informative and directly usable: weight correspondences, drop unreliable ones, or send more queries where the model is unsure. v2 has no equivalent output, so there is nothing to compare against.

## Slide 10
10
Abstaining on 20 percent of queries makes
v3 2.2x more accurate than v2
Why this is fair
Mean error is one operating point, and the only one v2 has.
Registration picks a few hundred points anyway, so abstaining is free.
1.06 px at 80% coverage
against v2 at 2.32
Same 2,348,000 queries as the calibration bins. Coverage = share of queries answered.
Notes: This is the slide I would most like your reaction to. The accuracy table earlier reports mean error over every pixel, which is the only operating point v2 has, because it cannot tell you which of its outputs to trust. v3 can, so instead of a point it has a curve. Discard the least confident fifth and error on what remains falls to 1.06 pixels against v2's 2.32 over the whole frame. More than twice as accurate over eighty percent of the image. Keep only the most confident fifth and it is 0.48. Why this is not a statistical trick: for registration and mapping you are choosing a few hundred points anyway, so declining to answer where the model is unsure costs you nothing you would otherwise have used.

## Slide 11
11
A fast platform meets three situations, and
flows a region rather than a frame
Left: the regions a tracker nominates. Right: the flow returned. Held-out VKITTI 2.
Notes: These are the three situations you described, on real frames. First, something worth flowing enters the field of view and you start tracking it. Second, the platform turns and that region now overlaps a second object. Third, a new object appears in a frame you are already part way through processing. On the right is what the model actually computes: flow inside the marked regions only. The grey area is not computed at all. That is the whole premise, and the next slides put numbers on what it costs and what you get back.

## Slide 12
12
Processing 14 percent of the frame costs
0.034 px and runs 4.4x faster
Region
Latency
Speedup
EPE
Full frame
33.3 ms
1.0x
0.657
Region, no margin
7.8 ms
4.3x
1.089
Region + 32 px
7.6 ms
4.4x
0.691
Region + 64 px
8.1 ms
4.1x
0.667
Region + 128 px
9.9 ms
3.4x
0.655
Design rule
margin ≈ expected motion
≈ speed / frame rate
The margin is not optional. Without one, error rises 65 percent and a quarter of
large-motion pixels fail outright, because global matching loses the context it
uses to locate distant correspondences.
Applies to any network in this family, v2 included: a platform technique, not a property of the decoder.
Notes: Here is what flowing only a region actually buys. Keep full resolution, process fourteen percent of the frame, and it costs thirty-four thousandths of a pixel. That is the enabling result for the whole scenario. The margin is the part worth dwelling on. Without one, error jumps sixty-five percent and a quarter of the large-motion pixels fail completely, because this network finds large displacement using attention over the whole image and a tight crop takes that away. I should be clear that this applies to any flow network including v2 unchanged. It is a platform technique, not something my decoder provides. What the decoder adds comes later.

## Slide 13
13
The margin a region needs is set by motion,
not by image size
Driving averages 26.6 px of motion and needs about 32 px of margin; aerial averages
9.26 px and needs about 8. Both shed most of the penalty by one frame of motion.
Measured with the baseline network. Agreement holds to a ratio of one; residuals beyond that differ by scene.
Notes: I wanted to know whether the margin rule was a curve fitted to one dataset or something more general, so I tested it on aerial sequences, which move very differently: nine point three pixels per frame against twenty-six point six for driving. The prediction was that the required margin should scale with motion, so the knee should move from thirty-two pixels down to about nine. It did. On the left the two need different absolute margins. On the right, divided by mean motion, both start at the same penalty and both have lost most of it by the point where the margin equals one frame of motion. I will be precise about the limits: the agreement is good up to that point and residuals differ beyond it, so this predicts the scale rather than the exact curve. That is still enough to size a margin from speed and frame rate before running anything.

## Slide 14
14
The same three situations in the aerial
domain, where motion is three times smaller
TartanAir aerial sequences. Same region geometry as the driving figure; no model trained on this domain.
Notes: The same three situations on aerial data, with the region geometry and the decoder configuration held identical. Only the domain changes. Two things to notice. The flow inside each region is much closer to uniform than in the driving frames, because a drone rotating through a static scene produces near-constant displacement over a small window. And no model in this study trained on this imagery, which is what makes the comparison on the next slide worth having.

## Slide 15
15
On a domain neither model trained for,
v3 leads at all seven margin settings
Crop margin
NeuFlow v2
NeuFlow v3
full frame
0.781
0.777
0 px
1.205
1.176
8 px
0.901
0.881
16 px
0.872
0.865
24 px
0.879
0.854
32 px
0.834
0.814
64 px
0.793
0.778
How much it counts
The only unconfounded comparison here: every other table is on a domain v3 trained on.
Consistent rather than large: 0.004 to 0.029 px, 40 pairs, one seed.
v3 is still worse on large-motion failures, 7.2% against 6.5%.
Mean end-point error, px. v2 trained on FlyingThings; v3 on FlyingChairs, VKITTI 2 and Sintel.
Notes: One result I did not expect. Everything else in this deck is measured on driving sequences, and v3 trained on driving data while v2 did not, which is a confound I have flagged throughout. Aerial data is neutral ground: neither model has seen anything like it. On that neutral ground v3 comes out ahead at all seven margin settings. The likely reason is that the decoder saw three datasets where v2 saw one, and the convex head is bounded so it cannot invent motion its inputs do not support, which should degrade more gracefully out of domain. I want to be careful about how much weight this carries: the margins are small, it is forty pairs and one seed, and v3 is still slightly worse on the large-motion pixels. What makes it worth showing is that it is consistent across seven independent settings.

## Slide 16
16
A region discovered mid-frame costs 1.7 ms,
against 7.3 ms for a fresh crop
The cached coarse state answers a question the platform did not have when the frame
arrived. A cropped pipeline must run a whole new pass, and is less accurate doing it.
Two disjoint crops cost more than one full frame, giving a simple policy: crop once, or not at all.
Notes: This is the third scenario, and the one result specific to this architecture rather than to cropping. A frame is already in flight when a new object enters the field of view. Because the coarse pass is cached, answering costs one point seven milliseconds. A cropped pipeline cannot reuse anything, since the new object is outside its box, so it runs a whole new pass at seven point three milliseconds, four times more, and the answer is worse, three point six pixels against two point one, because a fresh crop has lost the surrounding context. v2 keeps no state at all between calls. The general point is that this buys the ability to answer a question you did not know you would have when the frame arrived, which on a moving platform is most of them.

## Slide 17
17
The decoder earns its place when the
consumer chooses its own points
Use the decoder when
The consumer selects its own query points.
A frame is revisited after processing.
Each correspondence needs a confidence value.
Use the baseline when
One complete dense field per frame is consumed.
Nothing else is needed: v2 is more accurate and 10% faster there.
Selective prediction reframes the comparison: mean error over all pixels is the metric
the decoder loses on, and the only one a model without confidence can report.
Notes: So what is the contribution. It is an operating point, not a leaderboard position. For an application that consumes one complete dense field per frame and nothing else, v2 remains the correct choice and I will say so plainly: it is more accurate and ten percent faster in that mode. The decoder earns its place when the consumer picks its own points, revisits a frame, or needs a confidence value. And the selective prediction result reframes the whole accuracy comparison, because mean error over all pixels is exactly the metric a model without confidence is stuck with.

## Slide 18
18
The accuracy gap has a single cause, and
three experiments converge on it
Accuracy. The decoder’s finest input is 1/8 resolution; the upsampler it replaces reads the full-resolution frame.
Sub-pixel querying. For the same reason, evaluation between pixels is presently closer to interpolation than inference.
Embedded validation. All latency is from a laptop GPU; the edge premise is a design target, not a result.
Statistical resolution. One seed per configuration; differences below ~0.05 px are not resolved.
Three independent nulls point at the same mechanism: Fourier encoding, sub-pixel
querying, and reduced-resolution querying. The remedy is a full-resolution stem.
Notes: Limitations, stated plainly rather than buried. The accuracy gap is structural: the decoder never sees full-resolution features. Three separate experiments returned null for the same reason, which is what makes me confident in the diagnosis rather than merely suspicious. Sub-pixel querying is thinner than it sounds for the same reason: the interface is exact but the extra information recoverable between pixels is small until the decoder gets full-resolution input. There is no embedded measurement at all, so the word edge is a design target. And one seed per configuration, so please do not read much into differences below about five hundredths of a pixel.

## Slide 19
19
Conclusions
1. Queryable output is affordable. Arbitrary continuous coordinates in O(N), for 2.6% of mean accuracy, from a 13% smaller model.
2. Confidence is worth more than the mean. Abstaining on 20% of queries gives 2.2x lower error over the remaining 80% of the frame.
3. Region margins are predictable. Margin ≈ speed / frame rate, verified across a threefold difference in motion scale.
srinivasan.shrim@northeastern.edu | Code and report: github.com/shrirag10/Neuflowv3
Next: a full-resolution feature stem, then embedded measurement.
Notes: Three conclusions. Queryable output is affordable: arbitrary continuous coordinates for 2.6 percent of mean accuracy, from a smaller model. Confidence is worth more than the mean, because abstaining on a fifth of queries more than halves the error on the rest. And the region margin a fast platform needs is predictable from speed and frame rate before any flow is computed. The next experiment is the full-resolution stem, which is the direct attack on the one gap I have not closed. I will stop there. Are there questions or feedback?

## Slide 20
20
References
Zhang, Z., Gupta, A., Jiang, H., & Singh, H. (2024). NeuFlow v2: High-Efficiency Optical Flow Estimation on Edge Devices. arXiv:2408.10161.
Jung, H., Hui, Z., Luo, L., Yang, H., Liu, F., Yoo, S., Ranjan, R., & Demandolx, D. (2023). AnyFlow: Arbitrary Scale Optical Flow with Implicit Neural Representation. CVPR.
Teed, Z., & Deng, J. (2020). RAFT: Recurrent All-Pairs Field Transforms for Optical Flow. ECCV.
Yu et al. (2025). InfiniDepth: Implicit Neural Upsampling for Monocular Depth Estimation.
Kendall, A., & Gal, Y. (2017). What Uncertainties Do We Need in Bayesian Deep Learning for Computer Vision? NeurIPS.
Cabon, Y., Murray, N., & Humenberger, M. (2020). Virtual KITTI 2. arXiv:2001.10773.
Wang, W., Zhu, D., Wang, X., Hu, Y., Qiu, Y., Wang, C., Hu, Y., Kapoor, A., & Scherer, S. (2020). TartanAir: A Dataset to Push the Limits of Visual SLAM. IROS.
Notes: References for everything cited in the deck.

## Slide 21
Appendix A — Query cost and interface
21
Decode cost is flat to 2,048 queries:
2,048 points cost what 800 do
The entire API
state = model.infer_coarse_state(
img0, img1)
flow = model.decode_queries(
state, query_coords=q)
flow, b = ... return_uncertainty=True
Launch-overhead bound below ~10,000 points; compute-bound above, where dense mode wins.
1.254 ms at N = 800; 1.285 ms at N = 2,048. RTX 4060 laptop, fp16.
Notes: The interface is two calls: one coarse pass per frame pair, then as many decode calls as you like against it. The plot shows decode cost is flat between 800 and 2,048 queries, which tells you it is dominated by kernel launch overhead rather than arithmetic, so you get two thousand points for the price of eight hundred. Above about ten thousand points it becomes compute bound and dense mode is the better choice.

## Slide 22
Appendix B — Working implementation
22
The decoder runs as an interactive tool:
draw a region, get flow there
Two timed modes
QUERY decodes only inside the box against a full-frame coarse pass. Exact.
CROP feeds only the box through the pipeline, so cost scales with area, at the price of lost context.
The panel reports the measured breakdown live, including where the decoder is not the faster option.
Notes: This is a working tool, not a mock-up. Load a video, step to a frame, drag a box, and it computes flow in that box. Query mode runs the full coarse pass and decodes only inside the box, which is exact. Crop mode feeds just the box through the whole pipeline, so cost scales with the area requested but it loses the surrounding context that global matching uses. The panel shows the actual breakdown live, including the parts where v3 is not the faster option.

## Slide 23
Appendix C — Objectives set at the start
23
Two of three original objectives were not met;
the project delivers three others
Objective
Verdict
Evidence
Better accuracy than v2
not met
best 2.384 vs 2.324; like-for-like 7.6% behind
Less compute than v2
partly
dense 10% slower; repeat query 27x cheaper
Runs on edge devices
unproven
all figures from a laptop RTX 4060
What it does deliver
Queryable output
any continuous coordinate;
sparse equals dense exactly
Cheap repeat access
1.25 ms per further query
batch on a cached frame
Calibrated confidence
per-query error estimate,
monotonic against real error
Sparse-equals-dense verified to 0.00057 px maximum deviation.
Notes: The scorecard against what I set out to do, and two of three are not met. Better accuracy: not met. Less compute: partly, dense is slower, a first query is level, but repeat queries are twenty-seven times cheaper. Edge capable: unproven, everything is on a laptop 4060. What the project does deliver is the three things at the bottom, and those are measured.

## Slide 24
Appendix D — Anticipated questions
24
Four questions I expect, answered
Why is flow defined between pixels at all?
Motion is continuous; the pixel grid is a sampling artefact. A corner tracked to (312.7, 188.2) is a real answer, and registration consumes it directly.
Why freeze the backbone?
To isolate the decoder as the only variable. Unfreezing diverged at batch 4 and has not been retried at scale.
Why is dense v3 slower than v2?
v2 upsamples with one convolution that shares work across neighbouring pixels. v3 answers each query independently, giving up that sharing.
Is 2.6 percent worth the added complexity?
Not on its own. It is worth it if you need queryability, cheap repeat access, or confidence. For plain dense flow, v2 remains the better choice.
Notes: Pre-built answers to the questions I think are most likely.