## Slide 1
NeuFlow v3
Queryable optical flow for edge devices
Status update. NeuFlow v2 backbone (frozen) + an implicit decoder that answers
flow queries at arbitrary coordinates in O(N).
Shriman Raghav Srinivasan, MS Robotics, Northeastern University, Field Robotics Lab

## Slide 2
MOTIVATION
Why query optical flow?
Optical flow tells you where each pixel in frame t moves
to in frame t+1.
Current networks always produce the full dense map at a
fixed resolution. A lot of tasks never use most of it:
• registration wants a few hundred correspondences at
points it picks itself (corners, texture)
• sparse tracking only needs flow at feature points
• mosaicking needs matches in overlap regions, ideally
at sub-pixel positions
On a small GPU, computing 479k values to use 800 of them
is the difference between real time and not.
Idea
Keep everything in NeuFlow v2 that understands motion
(backbone, matching, refinement), frozen.
Swap only the last stage: instead of an upsampler that
always produces the full map, use a decoder that returns
flow at whatever coordinates you ask for.
Cost then scales with the number of queries, O(N),
instead of image area, O(HxW).
NeuFlow v3, S. Srinivasan
2

## Slide 3
METHOD
Pipeline: what stays from v2, what changes
NeuFlow v2
Image pair
(t, t+1)
CNN backbone
features at 1/8, 1/16
Cross-attention +
global matching (1/16)
Recurrent refinement
1 + 8 iterations
Coarse flow
at 1/8 scale
Convex upsampler
fixed 8× grid
Dense flow map
H × W, always
NeuFlow v3 (this work)
Image pair
(t, t+1)
CNN backbone
features at 1/8, 1/16
Cross-attention +
global matching (1/16)
Recurrent refinement
1 + 8 iterations
Coarse flow
at 1/8 scale
Implicit decoder
(next slide)
Flow at N requested
coordinates
Queries (x, y) — any
continuous positions
Identical to v2, weights frozen. matching quality inherited, not retrained
replaced stage (dark)
NeuFlow v3, S. Srinivasan
3

## Slide 4
METHOD
Inside the decoder
Query (x, y)
continuous pixel
coordinate
Sample 3×3 windows
from 4 feature maps:
context · 1/8 · 1/16 ·
warped frame-1
Gated hierarchical
fusion
(InfiniDepth Eq. 3)
MLP → softmax over
9 neighbors + bilinear
candidate (AnyFlow)
Convex blend of local
coarse-flow values
= flow(x, y)
Properties by construction, not by training
• Bounded output: the result is a weighted average of nearby coarse-flow values, so a bad weighting degrades
gracefully instead of producing garbage. (The earlier unbounded head never trained above its own init.)
• Exact init: bilinear interpolation is one particular weight setting, so the untrained decoder starts at 2.48 px EPE.
• The v2 upsampler is the fixed-grid special case of this mechanism, so v2 accuracy is reachable in principle.
NeuFlow v3, S. Srinivasan
4

## Slide 5
RESULTS
Starting point: no training at all
Input, VKITTI2 Scene18
Ground truth
NeuFlow v2, EPE 2.11 px
NeuFlow v3 untrained, EPE 2.26 px
No decoder training at all: the bilinear-prior init already produces usable flow (2.48 px EPE over the full validation set,
0.15 px behind v2), with querying functional and exact. Every training run afterwards had to beat this to be accepted.
NeuFlow v3, S. Srinivasan
5

## Slide 6
RESULTS
Trained on VKITTI2 only
Input, VKITTI2 Scene18
Ground truth
NeuFlow v2, EPE 2.11 px
NeuFlow v3 (VKITTI2-trained), EPE 2.07 px
Trained on 12,726 pairs: six VKITTI2 weather variants that share identical flow ground truth. Full-set result 2.39 px EPE,
the first checkpoint to improve on its own initialization, with no late-training collapse.
NeuFlow v3, S. Srinivasan
6

## Slide 7
RESULTS
Trained and evaluated on FlyingChairs
Input, chairs val 00006
Ground truth
NeuFlow v2, EPE 1.42 px
NeuFlow v3 (chairs), EPE 1.35 px
Across the 640 held-out chairs validation pairs: v2 2.24 px EPE (78.7% within 1 px), chairs-trained v3 2.40 px (76.6%).
The same model transfers to VKITTI2 driving scenes at 2.28 px, below v2 there, without ever seeing a road in training.
NeuFlow v3, S. Srinivasan
7

## Slide 8
RESULTS
Trained on both datasets jointly (best model)
Input, VKITTI2 Scene18
Ground truth
NeuFlow v2, EPE 2.11 px
NeuFlow v3 (mixed), EPE 2.06 px
Both datasets sampled together in every batch (34,958 pairs), evaluated on held-out VKITTI2: 2.18 px EPE, 6% better than v2,
76.4% within 1 px (v2: 77.6) and 3 px accuracy at parity. Sequential finetuning had failed at 2.50 px; joint sampling keeps both strengths.
NeuFlow v3, S. Srinivasan
8

## Slide 9
RESULTS
v2 vs v3 on the same input
NeuFlow v3, S. Srinivasan
9

## Slide 10
RESULTS
FlyingChairs examples
Large, varied synthetic displacements. the motion statistics that taught the decoder its error-tail robustness.
NeuFlow v3, S. Srinivasan
10

## Slide 11
RESULTS
Summary across training setups
Two informative negative results
Sequential finetuning (chairs, then VKITTI2)
reached 2.50 px. worse than either parent.
Joint sampling was the remedy, confirmed by
the mixed result.
Fourier position encoding changed nothing
(2.288 vs 2.275 px; 1 px accuracy identical).
The sub-pixel gap is therefore not caused
by missing positional information. one of
two candidate explanations eliminated by a
single controlled run.
NeuFlow v3, S. Srinivasan
11

## Slide 12
EFFICIENCY
Sparse vs dense, and what each costs
Dense output means the network computes flow for every pixel. 479,232 values for this input size. whether or not they are
needed. This is the only mode NeuFlow v2 has: its upsampler is a convolution that always produces the full map in one 37 ms pass.
Sparse output means computing flow only at N requested coordinates. Only v3 can do this: a 33 ms coarse pass shared by all queries,
then 1.6 ms per batch of up to ~2,000 points. The sparse values are not approximations. they equal the dense output exactly.
Reading the charts
Left: to get flow once, v2 dense
and v3 sparse cost the same
(~35 ms). v3 dense (327 ms) is an
evaluation mode, not a use case.
Right: once a pair is processed,
each further question costs v3
1.6 ms; v2 has no smaller unit of
work than the full 37 ms frame.
Video pipeline, 640x360 stream:
v3 sparse-800: 63.6 FPS
v2 dense: 60.3 FPS
v3 + motion boxes: 47.1 FPS
Parameters: 7.83 M (v3)
vs 9.03 M (v2).
NeuFlow v3, S. Srinivasan
12

## Slide 13
EFFICIENCY
FPS on a real video stream
Sixty frame pairs of a 640x360
YouTube driving video, decoded,
transferred, and processed -
identical frames for every mode.
v3 answering 800 targeted
queries per pair outpaces v2
producing its full map, and the
live motion-detection mode
holds 47 FPS. three times
faster than a typical 15 FPS
survey camera.
NeuFlow v3, S. Srinivasan
13

## Slide 14
INTERFACE
How to query the model
A query is one continuous (x, y) coordinate; sub-pixel
positions are valid inputs. N ranges from 1 to the full
frame (479,232 at 384x1248). Decode cost is flat at
1.6 ms up to roughly 2,000 queries per call.
state = model.infer_coarse_state(img0, img1) # once, 33 ms
flow = model.decode_queries(state, query_coords=q)
# q: [B, N, 2] pixel coords → [B, N, 2] flow
Training configuration: batch size 4 (8 GB VRAM budget);
4,096 supervision queries per image, half placed at motion
boundaries; AdamW with a one-cycle schedule peaking at
2e-4; backbone frozen throughout.
Interactive tool (PyQt5, in the repository):
• Click any pixel for its flow; grid, boundary-adaptive,
and dense-overlay modes; CSV export.
• Region window: drag a rectangle. flow computed
only inside the selection.
• Video and YouTube sources with frame stepping and
real-time playback: live flow-based motion boxes at
47 FPS (640x360), ego-motion compensated.
• System-resources tab: live FPS, latency, GPU, VRAM,
CPU, RAM graphs. VRAM stays flat while interacting.
NeuFlow v3, S. Srinivasan
14

## Slide 15
INTERFACE
The GUI
Adaptive queries over a dense overlay with the magnitude
legend. several hundred answers from one cached state.
Playback with live motion detection: the translating region
is boxed from the coarse flow at zero additional decode cost.
A model selector switches between v3 and the v2 baseline in place: with v2, every interaction requires the full dense map
to have been computed; with v3, the same interactions are answered from the cached coarse state in ~1.6 ms. The difference
between the two architectures is directly felt in the tool.
NeuFlow v3, S. Srinivasan
15

## Slide 16
INTERFACE
Live run on public video: motion detection with measurements
Forty consecutive frame pairs of a public YouTube highway video (640x360), processed live in the GUI: mean 29.8 FPS
end to end with motion boxes on the moving vehicles. The resource graphs were sampled during the same run; GPU memory
stays flat at 769 MB because one cached backbone state serves every interaction.
NeuFlow v3, S. Srinivasan
16

## Slide 17
V3 ACCELERATION
Attacking the frozen front-end: v3 sparse from 30 to 42 FPS
v3 inherits its 33 ms coarse pass from v2; 62% of it is refinement iterations that stop paying after four. At (2,4), sparse
mode runs 41.8 FPS (52% faster than v2 full frame) at better accuracy. Dense mode was rebuilt: window projections folded into
per-image convs (exact), fusion on the 1/8 grid, stride-2 decode. Full-frame v3: 29.9 ms vs v2 36.4 ms at equal EPE (2.284 vs
2.288), or 39.6 ms at clearly better EPE (2.245). v3 now beats v2 on its own dense workload. Gap left: 1px acc (75.7 vs 77.4).
NeuFlow v3, S. Srinivasan
17

## Slide 18
OBJECTIVES
Where the three goals stand
Goal 1, beat v2 accuracy. Done: 2.18 vs 2.32 px mean EPE (6% better) with mixed training.
1 px accuracy is within 1.2 points of v2 (76.4 vs 77.6) and 3 px is at parity.
Goal 2, less compute, edge-viable. Done for the sparse workload: same latency as a v2 full frame,
13% fewer parameters, ~2.2 GB VRAM at inference, and repeat queries about 20x cheaper than v2
recomputing. Dense-output mode stays slower; not the target use.
Goal 3, do what v2 cannot. Done: continuous-coordinate queries, output at any resolution, sparse
matches dense exactly, plus a working interactive tool.
NeuFlow v3, S. Srinivasan
18

## Slide 19
NEXT STEPS
Planned work and two requests
Request 1. HPC access
The Spring benchmark provides ground truth at twice the
input resolution (1080p images, 4K flow). Evaluating there
tests above-input-resolution querying. a question a
fixed-resolution network cannot even accept. Its working
set (hundreds of GB) and batch-scale training
exceed the 8 GB laptop GPU this work has used so far.
With HPC access, in order:
• Spring evaluation: v3 queried natively at 4K versus
v2 upsampled. the arbitrary-resolution claim, quantified
• FlyingThings3D pretraining (the standard second
second stage; 80 GB, batch 8–16)
• Longer mixed training at larger crops
Request 2. Field Robotics Lab survey data
The SeaBED AUV and UAV survey programs produce
exactly the data this method serves:
• Sequential seafloor transect imagery (50–75% overlap,
slow motion, fine texture). registration and mosaicking
with sparse on-demand queries; the fine-motion regime
also stresses sub-pixel accuracy directly.
• Nadir UAV survey sequences with GPS/IMU tags -
georegistration provides quantitative pseudo ground truth.
• Vehicle navigation (DVL/INS) and camera calibration -
reprojection-based flow ground truth on static scenes,
no manual labeling.
The ask is consecutive frames plus navigation data,
not finished mosaics.
NeuFlow v3, S. Srinivasan
19

## Slide 20
CURRENT WORK
Algorithm updates in training now (no results yet)
Five experiments queued on the university cluster (H200 GPUs, batch 16, 100K steps). All numbers pending: nothing below is a result until evaluated on the full validation set.
Refinement self-distillation
The 8-iteration refinement loop is 59% of runtime and iterations 5-8 barely change the answer. Retrain ONLY the refinement module so 3 iterations reproduce its own 8-iteration output (teacher = the frozen model itself, no ground truth). If it holds, v3 sparse goes from 30 to ~44 FPS with the decoder untouched.
Uncertainty head
One extra decoder output per query: the predicted error scale b. Trained by a self-calibrating loss (underestimate error and the loss explodes, overestimate and the log-penalty bites). Gives RANSAC/SLAM consumers a per-point trust signal and makes query selection principled. No baseline network offers this.
Scale-up at the deployment schedule
The mixed-data recipe retrained at batch 16, 100K steps, at the exact iteration schedule used in deployment, removing a train/eval mismatch present in earlier runs.
Fair-comparison training (grand mix)
Adds Sintel to the mix to approach v2 training distribution: addresses the data confound in current v3-vs-v2 accuracy claims.
Spring 1080p training
Prerequisite for the above-input-resolution evaluation (4K ground truth) that only a queryable decoder can take.
NeuFlow v3, S. Srinivasan
20

## Slide 21
CURRENT WORK
The two mechanisms, as flowcharts
Refinement self-distillation (trains only the refine module)
Image pair
Frozen model
8 iterations
Trainable copy
3 iterations
Teacher coarse flow
Student coarse flow
L1 difference
= training loss
No labels needed: the model supervises itself. Only the refinement weights update; backbone, matching and decoder stay frozen, so nothing already validated is at risk.
Uncertainty head (one extra output channel)
Query features
(fused, 260-d)
Head MLP
10 blend weights
-> flow (x, y)
1 scale channel
-> b = exp(s)
Training loss per query: |error| / b + 2 log b
If the head claims confidence (small b) and is wrong, the first term explodes; if it always claims ignorance (large b), the second term grows. The minimum is honest self-assessment: b learns to match the actual expected error. At initialization b = 1 px everywhere.
NeuFlow v3, S. Srinivasan
21

## Slide 22
METHOD
The complete algorithm, as pseudocode
# ONCE per image pair (~23 ms at 384x1248, RTX 4060)
f8, f16, ctx = backbone(I0, I1) # frozen v2
flow_s16 = global_match(cross_attn(f16))
for k in 1..K16: flow_s16 += refine16(corr(flow_s16), ctx)
flow_s8 = up2x(flow_s16)
for k in 1..K8: flow_s8 += refine8(corr(flow_s8), ctx)
state = {f8, f16, ctx, warp_map, flow_s8} # cached
# PER QUERY BATCH (~1.6 ms for up to ~2,000 points)
for each query (x, y): # continuous coords
feat = sample(state, x, y) # bilinear, 260-d
w[0..9], s = head(feat) # softmax weights + log-scale
cand = 3x3 coarse-flow neighborhood + bilinear value
flow = sum_i w[i] * cand[i] # bounded convex blend
b = exp(s) # predicted error, px
return flow[, b]
# TRAINING (decoder only; backbone frozen)
queries ~ 50% at flow-gradient boundaries, 50% uniform (N=4096)
loss = sum_iters gamma^(T-t) * L1(flow_t, GT) # gamma = 0.8
final iter with uncertainty: |err|/b + 2 log b # self-calibrating
NeuFlow v3, S. Srinivasan
22

## Slide 23
Q&A PREP
Questions I expect
Why is flow defined at non-integer coordinates? Bilinear interpolation makes feature maps continuous functions of position;
an MLP composed with them is defined at every real (x, y). Integer pixels are the special case dense maps hard-code.
Why freeze the backbone? Joint training is a moving-target problem requiring ~800K steps at InfiniDepth scale; at a 30K budget
the decoder diverges chasing shifting features (observed directly). Freezing also guarantees the v2 matching quality is inherited.
Is sparse output an approximation? No. It is the same function evaluated at fewer points; agreement with dense output is exact.
Why did out-of-domain training beat in-domain training? Mean EPE is dominated by the error tail. Diverse large motions train
tail robustness; five driving scenes train memorization. Joint training then combined both, as the mixed result shows.
What limits sub-pixel accuracy? Not positional information. measured (PE ablation, null result). Remaining candidates: the
1/8-scale coarse flow bounds recoverable detail, and large-motion training never supervises sub-pixel discrimination.
Why batch size 4? An 8 GB VRAM budget; the recipe is otherwise RAFT-standard and scales directly on larger GPUs.
NeuFlow v3, S. Srinivasan
23