## Slide 1
NeuFlow v3
Queryable optical flow for edge robotics
One frozen NeuFlow v2 backbone + an implicit decoder that answers flow queries at arbitrary (x, y) coordinates in O(N), not O(H×W).
Shriman Raghav Srinivasan · MS Robotics, Northeastern University · Field Robotics Lab

## Slide 2
MOTIVATION
Most tasks never use most of a dense flow map
Optical flow gives the motion of every pixel from frame t to t+1. Today's networks always emit the full map at a fixed resolution — even when the task wants a handful of points.
Registration a few hundred correspondences at self-chosen corners
Sparse tracking flow only at feature points, frame to frame
Mosaicking matches in overlap regions, at sub-pixel positions
On a small GPU, computing 479,232 values to use 800 of them is the difference between real time and not.
THE IDEA
Keep everything in v2 that understands motion — backbone, matching, refinement — frozen.
Swap only the last stage. Instead of an upsampler that always builds the full map, use a decoder that returns flow at whatever coordinates you ask for.
Cost scales with queries — O(N) not image area O(H×W).
NeuFlow v3 · S. Raghav Srinivasan · Field Robotics Lab, Northeastern
2

## Slide 3
METHOD · THE FOUNDATION
NeuFlow v2: real-time flow, kept frozen and untouched
Image
pair
CNN backbone
1/8 · 1/16 feats
Cross-attention
+ global match
Refine
×1 (1/16) · ×8 (1/8)
Coarse flow
1/8 resolution
Every block above is frozen in v3 — identical weights, identical computation. v3 inherits v2's matching quality by construction.
1
Shallow CNN — features at 1/8 and 1/16 scale
2
Cross-attention + global matching at 1/16 for the initial flow
3
Light recurrent refinement: 1 iteration at 1/16, 8 at 1/8
4
Learned convex upsampler — the one stage v3 replaces
v2 ALONE
9.03 M
parameters
19.6 ms
per frame pair (V100)
2.324 px
mean EPE, Virtual KITTI 2
Structural limit: resolution and cost are fixed at design time — no cheap way to ask a smaller question, no way to ask a finer one.
Zhang, Gupta, Jiang, Singh · arXiv:2408.10161
NeuFlow v3 · S. Raghav Srinivasan · Field Robotics Lab, Northeastern
3

## Slide 4
METHOD · THE CONTRIBUTION
A queryable decoder in place of the upsampler
The head outputs softmax weights over a 3×3 neighborhood of the coarse flow plus a bilinear candidate. The output is a bounded convex blend — it cannot hallucinate large flow. Zero-initialized, so an untrained decoder reproduces plain bilinear upsampling exactly (2.476 px EPE, step 0).
Two-pass API infer_coarse_state() once per pair, decode_queries() per batch
Exact sparse output matches dense at the same points to 0.00 px
Smaller 7.83 M params vs v2's 9.03 M — despite adding the capability
# ONCE per image pair (~16–17 ms)
coarse, feats = v2_pipeline(img0, img1) # frozen
# PER QUERY BATCH (~2.6 ms, up to ~2k pts)
for (x, y) in queries: # continuous
f = sample(feats, x, y) # bilinear
w,b = head(f) # softmax +b
cand = 3x3 coarse window + bilinear
flow = sum(w * cand) # bounded blend
return flow, b # b = per-query error
Bounded by construction · continuous coords · optional confidence out
NeuFlow v3 · S. Raghav Srinivasan · Field Robotics Lab, Northeastern
4

## Slide 5
METHOD · END-TO-END DATAFLOW
How a query becomes flow: the full v3 pipeline
PHASE 1 — once per image pair (~17 ms, frozen v2, cached)
Image pair
img0, img1
Frozen v2
backbone
CNN feats
1/8 · 1/16
Match +
refine
cross-attn,
8× recurrent
Coarse flow
+ features
cached
state
cached — reused by
every query, no recompute
PHASE 2 — per query batch (~2.6 ms for up to ~2,000 points, O(N))
Query (x, y)
any continuous
coord · N free
Sample
features
bilinear, 4
sources, 260-d
Convex head
(MLP)
softmax w + b
over 3×3 + bilin
Bounded
blend
Σ w·candidates
can't overshoot
Flow + b
per-point flow
+ confidence
features from the cached state feed the sampler
One backbone pass, then cheap repeated queries. The coarse state is computed once and cached; each query is an O(N) decode against it, so asking 5 more points costs ~2.6 ms, not another full pass.
NeuFlow v3 · S. Raghav Srinivasan · Field Robotics Lab, Northeastern
5

## Slide 6
RESULTS · ACCURACY
Every HPC checkpoint beats v2 on mean EPE
Chart: 
| v2 ref | grandmix | big18 | uncG
Mean EPE (px, lower is better) | 2.324 | 2.166 | 2.072 | 2.082
2.072 px
big18 — best to date. 11% better EPE than v2, at batch 16 / 100K steps. Scale was a real lever, not noise.
EPE
1px
3px
v2
2.324
77.6%
89.8%
big18
2.072
77.02%
89.91%
uncG
2.082
77.51%
90.02%
grandmix = FlyingChairs + Virtual KITTI 2 + MPI Sintel big18 = FlyingChairs + Virtual KITTI 2 uncG = big18 mix + uncertainty head
uncG beats v2 on 3px accuracy (90.02 vs 89.8); 1px gap down to 0.09 pts.

## Slide 7
RESULTS · SPEED
The real argument: v2 pays full price on every call
Chart: 
| First query on a new frame | Each additional query on the same frame
NeuFlow v2 (dense, every call) | 19.6 | 19.6
NeuFlow v3 (cached coarse state) | 19.1 | 2.6
~7.3×
faster on every repeat query — v2 has no cached state to reuse and must redo the full dense pass.
Measured, same V100
First query at parity: 19.1 vs 19.6 ms Decode cost flat across N=800 and N=2048 (2.6 ms) Dense-fast (stride 2): 45.7 FPS vs v2 5.8 FPS (~7.9×)
The pitch is not "6% better EPE" — it is that v3 pays once per frame, then answers follow-ups from cache. This directly answers the lab's original objection.
NeuFlow v3 · S. Raghav Srinivasan · Field Robotics Lab, Northeastern
6

## Slide 8
RESULTS · A CAPABILITY V2 CANNOT EXPRESS
A calibrated per-query confidence signal
One extra decoder output — a per-query error scale b, trained with a self-calibrating Laplace loss (|err|/b + log b). Binning 2.35 M points by predicted b, real error rises monotonically. The confidence output is not noise.
Chart: 
| bin 1 | bin 2 | bin 3 | bin 4 | bin 5
Real mean error (px) | 0.22 | 0.33 | 0.6 | 1.41 | 7.38
Predicted confidence bin (low b → high b)
r = 0.38 Pearson, predicted b vs real error
Validated contribution, independent of accuracy: real error climbs 0.22 → 7.38 px across bins, clean and monotonic. v2 cannot express per-point confidence at all. Open question: whether the auxiliary loss also regularizes the main flow output (uncG's edge). Single run — not yet proven.
NeuFlow v3 · S. Raghav Srinivasan · Field Robotics Lab, Northeastern
7

## Slide 9
RESULTS · REFINEMENT SELF-DISTILLATION
Distillation helps, but not enough end-to-end
The 8-iteration refinement loop is 59% of pipeline runtime, yet iterations 5–8 barely move the answer. Retrained only the refinement module — teacher = the model itself, no ground truth — so 3 iterations approach 8. Measured in isolation it looked strong; measured end-to-end through the real decoder, most of the gain disappeared.
Chart: 
| 3 iters (no distill) | 3 iters (distilled) | 8 iters (target)
EPE | 2.52 | 2.398 | 2.072
27% of the gap closed, end-to-end
0.122 of 0.448 px recovered end-to-end. The result, 2.398 px, still lands below v2 (2.324).
The lesson. The isolated coarse-flow test claimed 87.5%. End-to-end through a trained decoder, only 27% held. Deployable only if the decoder is retrained at 3 iterations — not done. Reported as a negative.
NeuFlow v3 · S. Raghav Srinivasan · Field Robotics Lab, Northeastern
8

## Slide 10
INTERFACE · HOW QUERIES WORK
Querying in practice: any N, and how training picks them
state = model.infer_coarse_state(img0, img1) # once per pair, ~17 ms flow = model.decode_queries(state, coords=q) # q: [B,N,2] -> [B,N,2]
A query is one continuous (x, y) — sub-pixel positions are valid. Decode cost is flat at ~2.6 ms for up to ~2,000 queries per call.
N ranges from 1 to the full frame
1
single GUI click 1.6 ms
800
registration demo 1.6 ms
2,048
edge sweet spot 2.6 ms
479,232
full dense frame ~293 ms
HOW TRAINING QUERIES ARE CHOSEN
1
4,096 per image
Each training step supervises 4,096 query points on a 256×512 crop — 3.1% of the crop's pixels. Enough signal to train the head cheaply; the decoder never sees a full dense map at train time.
2
50% boundaries, 50% uniform
Half the points are drawn at motion boundaries (a weight map built from the coarse-flow gradient, sampled by torch.multinomial), half uniformly at random. Boundaries are where flow is hardest and error concentrates — so supervision is spent where it matters.
3
3×3 coarse-flow window
Each query reads the 3×3 neighborhood of 1/8-res coarse flow around its cell. At 8× upsampling one coarse cell covers an 8×8 pixel block, so the true flow of any full-res pixel lies inside the convex hull of that cell + its 8 neighbors. The head blends those 9 (+ a bilinear candidate) — bounded by design.
NeuFlow v3 · S. Raghav Srinivasan · Field Robotics Lab, Northeastern
9

## Slide 11
INTERFACE · WORKING TOOL
An interactive GUI, and a live run on public video
Click to query
Adaptive queries over a dense overlay with magnitude legend; drag-select a region to decode only inside it.
Live motion detection
Playback boxes moving regions straight from the coarse flow — ego-motion subtracted, zero extra decode cost.
Model selector
Switch v3 ↔ v2 in place: v2 recomputes the full map every interaction; v3 reuses the cached coarse state.
29.8 FPS end-to-end
40 consecutive frame pairs of a public 640×360 YouTube highway video, processed live in the GUI with motion boxes on moving vehicles. GPU memory stays flat — one cached backbone state serves every interaction.
NeuFlow v3 · S. Raghav Srinivasan · Field Robotics Lab, Northeastern
10

## Slide 12
OBJECTIVES
Where the three goals stand
1
Beat v2 accuracy
DONE
Best EPE 2.072 vs 2.324 (11% better, big18). 3px now beats v2 (90.02 vs 89.8, uncG). 1px gap nearly closed (0.09 pts).
2
Less compute, edge-viable
DONE (sparse)
First query at parity on V100 (19.1 vs 19.6 ms); every additional query on the same frame ~7× cheaper — v2 has no cached state.
3
Do what v2 cannot
DONE
Continuous-coordinate queries, output at any resolution, sparse = dense exactly, an interactive tool, and a calibrated per-query confidence signal.
NeuFlow v3 · S. Raghav Srinivasan · Field Robotics Lab, Northeastern
11

## Slide 13
LIMITATIONS
What is not yet proven
1px accuracy Close but not fully closed on every checkpoint — grandmix still trails v2 by 1.35 pts; only uncG reaches within noise.
Training-data confound grandmix (FlyingChairs + Virtual KITTI 2 + MPI Sintel) was the fair-comparison attempt but scored below big18. Not closed until v2 is retrained on the same mixture.
Regularization claim uncG's apparent main-accuracy gain from the auxiliary loss is a single run — could be seed noise. Needs a repeat.
No edge-device data Every speed number is RTX 4060 / V100. No Jetson or embedded measurement exists yet.
Spring truncated Killed at 70K of 100K steps by the 8-h wall (2.080 EPE, strong). Never reached final LR anneal; the 4K-resolution query test has not run.
NeuFlow v3 · S. Raghav Srinivasan · Field Robotics Lab, Northeastern
12

## Slide 14
NEXT STEPS
Planned work, and two requests
IMMEDIATE
1
Merge distilled refinement with a trained decoder, evaluate end-to-end.
2
Resubmit Spring from step 70K to reach full 100K; run the 4K-GT query test only a queryable decoder can take.
3
Repeat the uncertainty-head run to test whether its accuracy gain is real or seed noise.
4
Retrain v2 on the grand-mix data to fully close the training-data confound.
REQUEST 1 — HPC access
The remaining runs (Spring resume, v2 retrain, repeat run) are 6–8 h jobs, done on Explorer so far. Continued access closes every open item above.
REQUEST 2 — Lab survey data
SeaBED AUV / UAV survey sequences (overlapping frames, slow motion, GPS/IMU tags) are exactly what this targets: sparse, on-demand correspondences at chosen points — not full dense flow over a whole seafloor mosaic.
NeuFlow v3 · S. Raghav Srinivasan · Field Robotics Lab, Northeastern
13

## Slide 15
One backbone pass. Correspondences on demand,
at the points you choose, at any resolution.
11% better EPE than v2 · 3px accuracy beats v2 · ~7× cheaper repeat queries · calibrated confidence v2 can't express
Shriman Raghav Srinivasan · github.com/shrirag10/Neuflowv3 · Field Robotics Lab, Northeastern